## Slide 1: Haptic implementation of the single reed pressure response.
MA. Maxwell Gentili-Morin
Using the TorqueTuner
Input Devices and Music Interaction Laboratory - IDML
MUMT 620 – Prof. Marcelo Wanderley
Notes: Hello!
Name
Bucket Brigade Devices
Currently doing research in the IDMIL Lab with Marcelo as an Undergrad!

## Slide 2: Concept
What is the single reed pressure response?
It is the flow of air going through the mouthpiece.
Dependent on the pressure difference between the mouth and the instruments cavity.
Represented by the simplified Bernoulli equation:
N. H. Fletcher and T. D. Rossing. The Physics of Musical Instruments. Springer-Verlag, New York, 1991.
Notes: Guitar Effect pedals
Analogy
Actual explanation

## Slide 3
Implementation
Analysis of the equation
Determined crucial variables (H, k)
Optimized curve for Implementation:
  Found the relation between H and k so that at zero flow, the pressure difference is 1
  Find the peak value in relation to k to H
Precompute the variables for the pressure and import them into a cpp header file.
Modeling the effect in python

## Slide 4
Implementation
Using the current firmware on the esp32, I created a mode, and implemented the function.
Simple as that.
Extending the TorqueTuner Firmware
int16_t Reed_Basic::calc(void* ptr){
  TorqueTuner* knob = (TorqueTuner*)ptr;
  float val = (H_init * rp_table[idx] - rp_B_table[idx]/k_init)*rp_sgn_table[idx];
  val *= -knob->scale;
  return static_cast<int16_t> (round(val));
}
int16_t Mode::calc_index(void* ptr) {
  TorqueTuner* knob = (TorqueTuner*)ptr;
  state += static_cast<int16_t> (round(knob->angle_delta * knob->stretch));
  if (wrap_haptics)
  {
  idx = mod(state, 3600);
  } else {
  idx = clip(state, 0, 3600);
  }
  return idx;
};

## Slide 5
Implementation
So as to have a simple method of testing the haptic effect, I pair it with the Linnstrument and a software called Surge XT
Demo Time
Incorporating it into a playable situation.

## Slide 6
Implementation
Current signal flow
Synth
Reed Model
Moteus
Linnstrument
Angle
Torque
Pressure
Flow
Flow
Note
Esp32
Max MSP
OSC

## Slide 7
Implementation
Signal flow
Reed Model
Linnstrument
Pressure
Torque
Esp32
H
K
Note
X
Y
Z
How would we map these?
Angle
Velocity

## Slide 8
Road to Final Project
Refine the haptic effect – create different modes with different intentions
Define meaningful and transparent mappings between variables
3D print a enclosure so that the Linnstrument and TorqueTuner can be held together.
Choose a fitting synthesis tool
Analyze how other interact with it.

## Slide 9
Q & A